## Slide 1: PPP Point-to-Point Protocol
CyberQuince

## Slide 2: Point-to-Point Protocol
PPP is a network protocol used to establish a direct connection between two nodes. It can provide authentication, transmission encryption, and compression.
Originally designed to work with serial connections, PPP was adopted by ISPs to provide dial up Internet access.
PPPoE, PPP over Ethernet, extends the original capability of PPP by encapsulating the packets in Ethernet frames.

## Slide 3: PPP – Authentication
PAP (Password Authentication Protocol) is the less secure method – passwords are transmitted in clear text.
CHAP (Challenge Handshake Authentication Protocol) still doesn’t use encryption, but it uses hashing. “Challenge” means that the credentials are checked periodically, even after the connection has been established.

## Slide 4: PPP – Configuration
GW(config)# username Int password cyber
Int(config)# username GW password cyber
GW(config)# interface serial 0/0/0
GW(config-if)# encapsulation ppp
GW(config-if)# ppp authentication chap
Int(config)# interface serial 0/0/0
Int(config-if)# encapsulation ppp
Int(config-if)# ppp authentication chap

## Slide 5: PPP Point-to-Point Protocol
CyberQuince